## Slide 1
TCP/IP Protocol Suite
<number>
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Chapter 15
Transmission
Control
Protocol (TCP)
Notes: <number>

## Slide 2: OBJECTIVES:
TCP/IP Protocol Suite
<number>
To introduce TCP as a protocol that provides reliable stream delivery service.
To define TCP features and compare them with UDP features.
To define the format of a TCP segment and its fields.
To show how TCP provides a connection-oriented service, and show the segments exchanged during connection establishment and connection termination phases.
To discuss the state transition diagram for TCP and discuss some scenarios.
To introduce windows in TCP that are used for flow and error control.
Notes: <number>

## Slide 3: OBJECTIVES (continued):
TCP/IP Protocol Suite
<number>
To discuss how TCP implements flow control in which the receive window controls the size of the send window.
To discuss error control and FSMs used by TCP during the data transmission phase.
To discuss how TCP controls the congestion in the network using different strategies.
To list and explain the purpose of each timer in TCP.
To discuss options in TCP and show how TCP can provide selective acknowledgment using the SACK option.
To give a layout and a simplified pseudocode for the TCP package.
Notes: <number>

## Slide 4
TCP/IP Protocol Suite
<number>
Chapter Outline
15.1 TCP Services
15.2 TCP Features
15.3 Segment
15.4 A TCP Connection
15.5 State Transition Diagram
15.6 Windows in TCP
15.7 Flow Control
15.8 Error Control
15.9 Congestion Control
15.10 TCP Timers
15.11 Options
15.12 TCP Package
Notes: <number>

## Slide 5
TCP/IP Protocol Suite
<number>
15-1 TCP SERVICES
Figure 15.1 shows the relationship of TCP to the other protocols in the TCP/IP protocol suite. TCP lies between the application layer and the network layer, and serves as the intermediary between the application programs and the network operations.
Notes: <number>

## Slide 6
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Process-to-Process Communication
Stream Delivery Service
Full-Duplex Communication
Multiplexing and Demultiplexing
Connection-Oriented Service
Reliable Service
Notes: <number>

## Slide 7
TCP/IP Protocol Suite
<number>
Figure 15.1 TCP/IP protocol suite
Notes: <number>

## Slide 8
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 9
TCP/IP Protocol Suite
<number>
Figure 15.2 Stream delivery
Notes: <number>

## Slide 10
TCP/IP Protocol Suite
<number>
Figure 15.3 Sending and receiving buffers
Notes: <number>

## Slide 11
TCP/IP Protocol Suite
<number>
Figure 15.4 TCP segments
Notes: <number>

## Slide 12
TCP/IP Protocol Suite
<number>
15-2 TCP FEATURES
To provide the services mentioned in the previous section, TCP has several features that are briefly summarized in this section and discussed later in detail.
Notes: <number>

## Slide 13
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Numbering System
Flow Control
Error Control
Congestion Control
Notes: <number>

## Slide 14
TCP/IP Protocol Suite
<number>
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with an arbitrarily generated number.
Note
Notes: <number>

## Slide 15
TCP/IP Protocol Suite
<number>
Suppose a TCP connection is transferring a file of 5,000 bytes. The first byte is numbered 10,001. What are the sequence numbers for each segment if data are sent in five segments, each carrying 1,000 bytes?
Solution
The following shows the sequence number for each segment:
Example 15.1
Notes: <number>

## Slide 16
TCP/IP Protocol Suite
<number>
The value in the sequence number field of a segment defines the number assigned to the first data byte contained in that segment.
Note
Notes: <number>

## Slide 17
TCP/IP Protocol Suite
<number>
The value of the acknowledgment field in a segment defines the number of the next byte a party expects to receive.
The acknowledgment number is cumulative.
Note
Notes: <number>

## Slide 18
TCP/IP Protocol Suite
<number>
15-3 SEGMENT
Before discussing TCP in more detail, let us discuss the TCP packets themselves. A packet in TCP is called a segment.
Notes: <number>

## Slide 19
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Format
Encapsulation
Notes: <number>

## Slide 20
TCP/IP Protocol Suite
<number>
Figure 15.5 TCP segment format
Notes: <number>

## Slide 21
TCP/IP Protocol Suite
<number>
Figure 15.6 Control field
Notes: <number>

## Slide 22
TCP/IP Protocol Suite
<number>
Figure 15.7 Pseudoheader added to the TCP segment
Notes: <number>

## Slide 23
TCP/IP Protocol Suite
<number>
The use of the checksum in TCP is mandatory.
Note
Notes: <number>

## Slide 24
TCP/IP Protocol Suite
<number>
Figure 15.8 Encapsulation
Notes: <number>

## Slide 25
TCP/IP Protocol Suite
<number>
15-4 A TCP CONNECTION
TCP is connection-oriented. It establishes a virtual path between the source and destination. All of the segments belonging to a message are then sent over this virtual path. You may wonder how TCP, which uses the services of IP, a connectionless protocol, can be connection-oriented. The point is that a TCP connection is virtual, not physical. TCP operates at a higher level. TCP uses the services of IP to deliver individual segments to the receiver, but it controls the connection itself. If a segment is lost or corrupted, it is retransmitted.
Notes: <number>

## Slide 26
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Connection Establishment
Data Transfer
Connection Termination
Connection Reset
Notes: <number>

## Slide 27
TCP/IP Protocol Suite
<number>
Figure 15.9 Connection establishment using three-way handshake
Means “no data” !
seq: 8001 if piggybacking
Notes: <number>

## Slide 28
TCP/IP Protocol Suite
<number>
A SYN segment cannot carry data, but it consumes one sequence number.
Note
Notes: <number>

## Slide 29
TCP/IP Protocol Suite
<number>
A SYN + ACK segment cannot carry data, but does consume one sequence number.
Note
Notes: <number>

## Slide 30
TCP/IP Protocol Suite
<number>
An ACK segment, if carrying no data, consumes no sequence number.
Note
Notes: <number>

## Slide 31
TCP/IP Protocol Suite
<number>
Figure 15.10 Data Transfer
Pushing data
Urgent data
Notes: <number>

## Slide 32
TCP/IP Protocol Suite
<number>
Figure 15.11 Connection termination using three-way handshake
Notes: <number>

## Slide 33
TCP/IP Protocol Suite
<number>
The FIN segment consumes one sequence number if it does not carry data.
Note
Notes: <number>

## Slide 34
TCP/IP Protocol Suite
<number>
The FIN + ACK segment consumes one sequence number if it does not carry data.
Note
Notes: <number>

## Slide 35
TCP/IP Protocol Suite
<number>
Figure 15.12 Half-Close
Notes: <number>

## Slide 36
TCP/IP Protocol Suite
<number>
15-5 STATE TRANSITION DIAGRAM
To keep track of all the different events happening during connection establishment, connection termination, and data transfer, TCP is specified as the finite state machine shown in Figure 15.13.
Notes: <number>

## Slide 37
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Scenarios
Notes: <number>

## Slide 38
TCP/IP Protocol Suite
<number>
Figure 15.13 State transition diagram
Notes: <number>

## Slide 39
TCP/IP Protocol Suite
<number>
The state marked as ESTBLISHED in the FSM is in fact two different
sets of states that the client and server undergo to transfer data.
Note
Notes: <number>

## Slide 40
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 41
TCP/IP Protocol Suite
<number>
Figure 15.14 Transition diagram for connection and half-close termination
Notes: <number>

## Slide 42
TCP/IP Protocol Suite
<number>
Figure 15.15 Time-line diagram for Figure 15.14
1. Enough time for an ACK to be lost and a new FIN to arrive. If during the TIME-WAIT state, a new FIN arrives, the client sends a new ACK and restarts the 2MSL timer
To prevent a duplicate segment from one connection appearing in the next one, TCP requires that incarnation cannot take place unless 2MSL amount of time has elapsed.
Another solution: the ISN of the incarnation is greater than the last seq. # used in the previous connection.
Notes: <number>

## Slide 43
TCP/IP Protocol Suite
<number>
Figure 15.16 Transition diagram for a common scenario
Notes: <number>

## Slide 44
TCP/IP Protocol Suite
<number>
Figure 15.17 Time line for a common scenario
Notes: <number>

## Slide 45
TCP/IP Protocol Suite
<number>
Figure 15.18 Simultaneous open
Notes: <number>

## Slide 46
TCP/IP Protocol Suite
<number>
Figure 15.19 Simultaneous close
ex
Notes: <number>

## Slide 47
TCP/IP Protocol Suite
<number>
Figure 15.20 Denying a connection
Notes: <number>

## Slide 48
TCP/IP Protocol Suite
<number>
Figure 15.21 Aborting a connection
Notes: <number>

## Slide 49
TCP/IP Protocol Suite
<number>
15-6 WINDOWS IN TCP
Before discussing data transfer in TCP and the issues such as flow, error, and congestion control, we describe the windows used in TCP. TCP uses two windows (send window and receive window) for each direction of data transfer, which means four windows for a bidirectional communication. To make the discussion simple, we make an assumption that communication is only unidirectional; the bidirectional communication can be inferred using two unidirectional communications with piggybacking.
Notes: <number>

## Slide 50
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Send Window
Receive Window
Notes: <number>

## Slide 51
TCP/IP Protocol Suite
<number>
Figure 15.22 Send window in TCP
Notes: <number>

## Slide 52
TCP/IP Protocol Suite
<number>
Figure 15.23 Receive window in TCP
Notes: <number>

## Slide 53
TCP/IP Protocol Suite
<number>
15-7 FLOW CONTROL
As discussed in Chapter 13, flow control balances the rate a producer creates data with the rate a consumer can use the data. TCP separates flow control from error control. In this section we discuss flow control, ignoring error control. We temporarily assume that the logical channel between the sending and receiving TCP is error-free. Figure 15.24 shows unidirectional data transfer between a sender and a receiver; bidirectional data transfer can be deduced from unidirectional one as discussed in Chapter 13.
Notes: <number>

## Slide 54
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Opening and Closing Windows
Shrinking of Windows
Silly Window Syndrome
Notes: <number>

## Slide 55
TCP/IP Protocol Suite
<number>
Figure 15.24 TCP/IP protocol suite
Notes: <number>

## Slide 56
TCP/IP Protocol Suite
<number>
Figure 15.25 An example of flow control
Notes: <number>

## Slide 57
TCP/IP Protocol Suite
<number>
Figure 15.26 shows the reason for the mandate in window shrinking. Part a of the figure shows values of last acknowledgment and rwnd. Part b shows the situation in which the sender has sent bytes 206 to 214. Bytes 206 to 209 are acknowledged and purged. The new advertisement, however, defines the new value of rwnd as 4, in which 210 + 4 < 206 + 12. When the send window shrinks, it creates a problem: byte 214 which has been already sent is outside the window. The relation discussed before forces the receiver to maintain the right-hand wall of the window to be as shown in part a because the receiver does not know which of the bytes 210 to 217 has already been sent. One way to prevent this situation is to let the receiver postpone its feedback until enough buffer locations are available in its window. In other words, the receiver should wait until more bytes are consumed by its process.
Example 15.2
Notes: <number>

## Slide 58
TCP/IP Protocol Suite
<number>
Figure 15.26 Example 15.2
210
Prevent the shrinking of the send window:
new ackNo + new rwnd >= last ackNo + last rwnd
?
Notes: <number>

## Slide 59: Silly Window Syndrome (1)
TCP/IP Protocol Suite
<number>
Sending data in very small segments
Syndrome created by the Sender
  Sending application program creates data slowly (e.g. 1 byte at a time)
  Wait and collect data to send in a larger block
  How long should the sending TCP wait?
  Solution: Nagle’s algorithm
  Nagle’s algorithm takes into account (1) the speed of the application program that creates the data, and (2) the speed of the network that transports the data

## Slide 60: Silly Window Syndrome (2)
TCP/IP Protocol Suite
<number>
Syndrome created by the Receiver
  Receiving application program consumes data slowly (e.g. 1 byte at a time)
  The receiving TCP announces a window size of 1 byte. The sending TCP sends only 1 byte…
  Solution 1: Clark’s solution
  Sending an ACK but announcing a window size of zero until there is enough space to accommodate a segment of max. size or until half of the buffer is empty

## Slide 61: Silly Window Syndrome (3)
TCP/IP Protocol Suite
<number>
  Solution 2: Delayed Acknowledgement
  The receiver waits until there is decent amount of space in its incoming buffer before acknowledging the arrived segments
  The delayed acknowledgement prevents the sending TCP from sliding its window. It also reduces traffic.
  Disadvantage: it may force the sender to retransmit the unacknowledged segments
  To balance: should not be delayed by more than 500ms

## Slide 62
TCP/IP Protocol Suite
<number>
15-8 ERROR CONTROL
TCP is a reliable transport layer protocol. This means that an application program that delivers a stream of data to TCP relies on TCP to deliver the entire stream to the application program on the other end in order, without error, and without any part lost or duplicated.
Error control in TCP is achieved through the use of three tools: checksum, acknowledgment, and time-out.
Notes: <number>

## Slide 63
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Checksum
Acknowledgment
Retransmission
Out-of-Order Segments
FSMs for Data Transfer in TCP
Some Scenarios
Notes: <number>

## Slide 64
TCP/IP Protocol Suite
<number>
ACK segments do not consume sequence numbers and
are not acknowledged.
Note
Notes: <number>

## Slide 65: Acknowledgement Type
TCP/IP Protocol Suite
<number>
  In the past, TCP used only one type of acknowledgement: Accumulative Acknowledgement (ACK), also namely accumulative positive acknowledgement
  More and more implementations are adding another type of acknowledgement: Selective Acknowledgement (SACK), SACK is implemented as an option at the end of the TCP header.

## Slide 66
TCP/IP Protocol Suite
<number>
Data may arrive out of order and be temporarily stored by the receiving TCP,
but TCP guarantees that no out-of-order data are delivered to the process.
Note
Notes: <number>

## Slide 67
TCP/IP Protocol Suite
<number>
TCP can be best modeled as a Selective Repeat protocol.
Note
Notes: <number>

## Slide 68
TCP/IP Protocol Suite
<number>
Figure 15.27 Simplified FSM for sender site
Notes: <number>

## Slide 69
TCP/IP Protocol Suite
<number>
Figure 15.28 Simplified FSM for the receiver site
Notes: <number>

## Slide 70: Rules for Generating ACK (1)
TCP/IP Protocol Suite
<number>
  1. When one end sends a data segment to the other end, it must include an ACK. That gives the next sequence number it expects to receive. (Piggyback)
  2. The receiver needs to delay sending (until another segment arrives or 500ms) an ACK segment if there is only one outstanding in-order segment. It prevents ACK segments from creating extra traffic.
  3. There should not be more than 2 in-order unacknowledged segments at any time. It prevent the unnecessary retransmission

## Slide 71: Rules for Generating ACK (2)
TCP/IP Protocol Suite
<number>
  4. When a segment arrives with an out-of-order sequence number that is higher than expected, the receiver immediately sends an ACK segment announcing the sequence number of the next expected segment. (for fast retransmission)
  5. When a missing segment arrives, the receiver sends an ACK segment to announce the next sequence number expected.
  6. If a duplicate segment arrives, the receiver immediately sends an ACK.

## Slide 72
TCP/IP Protocol Suite
<number>
Figure 15.29 Normal operation
Notes: <number>

## Slide 73
TCP/IP Protocol Suite
<number>
Figure 15.30 Lost segment
Notes: <number>

## Slide 74
TCP/IP Protocol Suite
<number>
The receiver TCP delivers only ordered data to the process.
Note
Notes: <number>

## Slide 75
TCP/IP Protocol Suite
<number>
Figure 15.31 Fast retransmission
Notes: <number>

## Slide 76
TCP/IP Protocol Suite
<number>
Figure 15.32 Lost acknowledgment
Notes: <number>

## Slide 77
TCP/IP Protocol Suite
<number>
Figure 15.33 Lost acknowledgment corrected by resending a segment
Notes: <number>

## Slide 78
TCP/IP Protocol Suite
<number>
Lost acknowledgments may create deadlock if they are not
properly handled.
Note
Notes: <number>

## Slide 79
TCP/IP Protocol Suite
<number>
15-9 CONGESTION CONTROL
We discussed congestion control in Chapter 13. Congestion control in TCP is based on both open loop and closed-loop mechanisms. TCP uses a congestion window and a congestion policy that avoid congestion and detect and alleviate congestion after it has occurred.
Notes: <number>

## Slide 80
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Congestion Window
Congestion Policy
Notes: <number>

## Slide 81
TCP/IP Protocol Suite
<number>
Figure 15.34 Slow start, exponential increase
Notes: <number>

## Slide 82
TCP/IP Protocol Suite
<number>
In the slow start algorithm, the size of the congestion window increases exponentially until it reaches a threshold.
Note
Notes: <number>

## Slide 83
TCP/IP Protocol Suite
<number>
Figure 15.35 Congestion avoidance, additive increase
Notes: <number>

## Slide 84
TCP/IP Protocol Suite
<number>
In the congestion avoidance algorithm the size of the congestion window
increases additively until
congestion is detected.
Note
Notes: <number>

## Slide 85
TCP/IP Protocol Suite
<number>
Figure 15.36 TCP Congestion policy summary
Notes: <number>

## Slide 86
TCP/IP Protocol Suite
<number>
Figure 15.37 Congestion example
Notes: <number>

## Slide 87
TCP/IP Protocol Suite
<number>
15-10 TCP TIMERS
To perform its operation smoothly, most TCP implementations use at least four timers as shown in Figure 15.38 (slide 83).
Notes: <number>

## Slide 88
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Retransmission Timer
Persistence Timer
Keepalive Timer
TIME-WAIT Timer
Notes: <number>

## Slide 89
TCP/IP Protocol Suite
<number>
Figure 15.38 TCP timers
Notes: <number>

## Slide 90
TCP/IP Protocol Suite
<number>
In TCP, there can be only one RTT measurement in progress at any time.
Note
Since the segments and their ACKs do not have a 1-1 relationship
Notes: <number>

## Slide 91: Calculation of RTO (1)
TCP/IP Protocol Suite
<number>
Smoothed RTT: RTTS
  Original 🡪 No value
  After 1st measurement 🡪 RTTS = RTTM
  2nd … 🡪 RTTS = (1-α)*RTTS + α*RTTM
RTT Deviation : RTTD
  Original 🡪 No value
  After 1st measurement 🡪 RTTD = 0.5*RTTM
  2nd … 🡪 RTTD = (1-β)*RTTD + β*|RTTS - RTTM|

## Slide 92: Calculation of RTO (2)
TCP/IP Protocol Suite
<number>
Retransmission Timeout (RTO)
  Original 🡪 Initial value
  After any measurement 🡪 RTO = RTTS + 4RTTD
Example 10 (page 322)
  α = 1/8
  β = 1/4

## Slide 93
TCP/IP Protocol Suite
<number>
Let us give a hypothetical example. Figure 15.39 shows part of a connection. The figure shows the connection establishment and part of the data transfer phases.
1. When the SYN segment is sent, there is no value for RTTM, RTTS, or RTTD. The value of RTO is set to 6.00 seconds. The following shows the value of these variable at this moment:
Example 15.3
2. When the SYN+ACK segment arrives, RTTM is measured and is equal to 1.5 seconds.
Notes: <number>

## Slide 94
TCP/IP Protocol Suite
<number>
3. When the first data segment is sent, a new RTT measurement starts. No RTT measurement starts for the second data segment because a measurement is already in progress. The arrival of the last ACK segment is used to calculate the next value of RTTM. Although the last ACK segment acknowledges both data segments (cumulative), its arrival finalizes the value of RTTM for the first segment. The values of these variables are now as shown below.
Example 15.3 Continued
Notes: <number>

## Slide 95
TCP/IP Protocol Suite
<number>
Figure 15.39 Example 15.3
Notes: <number>

## Slide 96
TCP/IP Protocol Suite
<number>
TCP does not consider the RTT of a retransmitted segment in its calculation of a new RTO.
Note
Notes: <number>

## Slide 97
TCP/IP Protocol Suite
<number>
Figure 15.40 is a continuation of the previous example. There is retransmission and Karn’s algorithm is applied.
The first segment in the figure is sent, but lost. The RTO timer expires after 4.74 seconds. The segment is retransmitted and the timer is set to 9.48, twice the previous value of RTO. This time an ACK is received before the time-out. We wait until we send a new segment and receive the ACK for it before recalculating the RTO (Karn’s algorithm).
Example 15.4
Notes: <number>

## Slide 98
TCP/IP Protocol Suite
<number>
Figure 15.40 Example 15.4
Notes: <number>

## Slide 99
TCP/IP Protocol Suite
<number>
15-11 OPTIONS
The TCP header can have up to 40 bytes of optional information. Options convey additional information to the destination or align other options. We can define two categories of options: 1-byte options and multiple-byte options. The first category contains two types of options: end of option list and no operation. The second category, in most implementations, contains five types of options: maximum segment size, window scale factor, timestamp, SACK-permitted, and SACK (see Figure 15.41).
Notes: <number>

## Slide 100
TCP/IP Protocol Suite
<number>
Figure 15.41 Options
Notes: <number>

## Slide 101
TCP/IP Protocol Suite
<number>
Figure 15.42 End-of-option option
Notes: <number>

## Slide 102
TCP/IP Protocol Suite
<number>
EOP can be used only once.
Note
Notes: <number>

## Slide 103
TCP/IP Protocol Suite
<number>
Figure 15.43 No-operation option
Notes: <number>

## Slide 104
TCP/IP Protocol Suite
<number>
NOP can be used more than once.
Note
Notes: <number>

## Slide 105
TCP/IP Protocol Suite
<number>
Figure 15.44 Minimum-segment-size option
Notes: <number>

## Slide 106
TCP/IP Protocol Suite
<number>
The value of MSS is determined during connection establishment and does not change during the connection.
Note
Notes: <number>

## Slide 107
TCP/IP Protocol Suite
<number>
Figure 15.45 Window-scale-factor option
Notes: <number>

## Slide 108
TCP/IP Protocol Suite
<number>
The value of the window scale factor can be determined only during connection
establishment; it does not change during the connection.
Note
Notes: <number>

## Slide 109
TCP/IP Protocol Suite
<number>
Figure 15.46 Timestamp option
Notes: <number>

## Slide 110
TCP/IP Protocol Suite
<number>
One application of the timestamp option is the calculation of round-trip time (RTT).
Note
Notes: <number>

## Slide 111
TCP/IP Protocol Suite
<number>
Figure 15.47 shows an example that calculates the round-trip time for one end. Everything must be flipped if we want to calculate the RTT for the other end.
Example 15.5
Notes: <number>

## Slide 112
TCP/IP Protocol Suite
<number>
Figure 15.47 Example 15.5
Notes: <number>

## Slide 113
TCP/IP Protocol Suite
<number>
The timestamp option can also be used for PAWS.
Note
Notes: <number>

## Slide 114
TCP/IP Protocol Suite
<number>
Figure 15.48 SACK
Notes: <number>

## Slide 115
TCP/IP Protocol Suite
<number>
Let us see how the SACK option is used to list out-of-order blocks. In Figure 15.49 an end has received five segments of data.
Example 15.6
Notes: <number>

## Slide 116
TCP/IP Protocol Suite
<number>
Figure 15.49 Example 15.6
Notes: <number>

## Slide 117
TCP/IP Protocol Suite
<number>
Figure 15.50 shows how a duplicate segment can be detected with a combination of ACK and SACK. In this case, we have some out-of-order segments (in one block) and one duplicate segment. To show both out-of-order and duplicate data, SACK uses the first block, in this case, to show the duplicate data and other blocks to show out-of-order data. Note that only the first block can be used for duplicate data. The natural question is how the sender, when it receives these ACK and SACK values, knows that the first block is for duplicate data (compare this example with the previous example). The answer is that the bytes in the first block are already acknowledged in the ACK field; therefore, this block must be a duplicate.
Example 15.7
Notes: <number>

## Slide 118
TCP/IP Protocol Suite
<number>
Figure 15.50 Example 15.7
Notes: <number>

## Slide 119
TCP/IP Protocol Suite
<number>
Figure 15.51 shows what happens if one of the segments in the out-of-order section is also duplicated. In this example, one of the segments (4001:5000) is duplicated.
The SACK option announces this duplicate data first and then the out-of-order block. This time, however, the duplicated block is not yet acknowledged by ACK, but because it is part of the out-of-order block (4001:5000 is part of 4001:6000), it is understood by the sender that it defines the duplicate data.
Example 15.8
Notes: <number>

## Slide 120
TCP/IP Protocol Suite
<number>
Figure 15.51 Example 15.8
Notes: <number>

## Slide 121
TCP/IP Protocol Suite
<number>
15-12 TCP PACKAGE
The TCP header can have up to 40 bytes of optional information. Options convey additional information to the destination or align other options. We can define two categories of options: 1-byte options and multiple-byte options. The first category contains two types of options: end of option list and no operation. The second category, in most implementations, contains five types of options: maximum segment size, window scale factor, timestamp, SACK-permitted, and SACK (see Figure 15.41).
Notes: <number>

## Slide 122
TCP/IP Protocol Suite
<number>
Topics Discussed in the Section
Transmission Control Block TCBs
Timers
Main Module
Input Processing Module
Output Processing Module
Notes: <number>

## Slide 123
TCP/IP Protocol Suite
<number>
Figure 15.52 TCBs
Notes: <number>

## Slide 124
TCP/IP Protocol Suite
<number>
Figure 15.53 TCP/IP protocol suite
Notes: <number>

## Slide 125
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 126
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 127
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 128
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 129
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 130
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 131
TCP/IP Protocol Suite
<number>
Notes: <number>

## Slide 132
TCP/IP Protocol Suite
<number>
Notes: <number>